## Slide 1: Build CPU in 1 Month
Lecture 01

## Slide 2: To-Do Lists
Intro
  Grammar(Verilog and SystemVerilog)
  Architecture
  Toolchain
Hand on
  Why our simulation don’t pass?
  Let’s add inst. and run simulation again
  Run monitor program
About the course assignment
  How to accomplish it

## Slide 3: Grammar(Verilog and SystemVerilog)
adder.v
wire reg
always @(*)
always @(posedge clk)
adder.sv
logic
always_comb
always_ff @(posedge clk)
support other data types, enum …
especially for verification
sv 是从 Verilog 扩展而来，也支持 Verilog 的一些语法，都属于经典的 HDL(Hardware Description Language)

## Slide 4: Grammar(Verilog and SystemVerilog)
declare variable（声明变量）
logic [31 : 0] a, b, c; logic [31 : 0] mem [1023 : 0];
process block（过程块）
  combinational logic
  always_comb begin
  c = a + b;
  end
  sequential logic
  always_ff @(posedge clk) begin
  c <= a + b;
  end

## Slide 5: Grammar(Verilog and SystemVerilog)
ternary expression（三元表达式）
logic a, b, c, sel_a;
always_comb begin
c = sel_a ? a : b;
end
if else
always_comb begin
if (sel_a) c = a;
else c = b;
end
MUX
a
b
sel_a
c
MUX
a
b
sel_a
a
LOOP!!!

## Slide 6: 从 Github 上获取工程文件