## Slide 1: Build CPU in 1 Month
Lecture 01

## Slide 2: To-Do Lists
Intro
  Grammar(Verilog and SystemVerilog)
  Architecture
  Toolchain
Hand on
  Why our simulation don’t pass?
  Add instruction
  Run monitor program
Course assignment
  Advice for report

## Slide 3: Grammar(Verilog and SystemVerilog)
adder.v
wire reg
always @(*)
always @(posedge clk)
adder.sv
logic
always_comb
always_ff @(posedge clk)
support other data types, enum …
especially for verification
SystemVerilog 是从 Verilog 扩展而来，也支持 Verilog 的一些语法，都属于经典的 HDL(Hardware Description Language)

## Slide 4: Grammar(Verilog and SystemVerilog)
declare variable（声明变量）
logic [31 : 0] a, b, c; logic [31 : 0] mem [1023 : 0];
process block（过程块）
  combinational logic
  always_comb begin
  c = a + b;
  end
  sequential logic
  always_ff @(posedge clk) begin
  c <= a + b;
  end

## Slide 5: Grammar(Verilog and SystemVerilog)
case
always_comb begin
case (sel_a)
1'b1 : c = a;
1'b0 : c = b;
default : c = a;
endcase
end
ternary expression（三元表达式）
logic a, b, c, sel_a;
always_comb begin
c = sel_a ? a : b;
end
if else
always_comb begin
if (sel_a) c = a;
else c = b;
end
MUX
a
b
sel_a
c
MUX
a
b
sel_a
a
LOOP!!!

## Slide 6: To-Do Lists
Intro
  Grammar(Verilog and SystemVerilog)
  Architecture
  Toolchain
Hand on
  Why our simulation don’t pass?
  Add instruction
  Run monitor program
Course assignment
  Advice for report

## Slide 7: Architecture
5-stage pipeline CPU
  classical micro-architecture and memory connected with bus
PC
IF
ifid
idexe
exemen
memwb
ID
EXE
MEM
WB
BUS
Kernel
code
Kernel
data
User
code
User
data
Serial
port
REG
FILE
STALL

## Slide 8: Architecture
Bus（总线）
  定义：一组物理线和连接器的集合，计算机组件间交换数据常用的一种标准规范，处理器、内存、I/O传递信息的公用通道。总之，主机各部件通过总线连接，外设通过相应接口电路与总线连接
  基本功能：在多个设备间搭建一条数据通路，响应每个设备的请求
Core
Kernel code
Kernel data
User code
User data
Serial port
inst REQ
data REQ
Bus
Arbiter
Address Decode

## Slide 9: To-Do Lists
Intro
  Grammar(Verilog and SystemVerilog)
  Architecture
  Toolchain
Hand on
  Why our simulation don’t pass?
  Add instruction
  Run monitor program
Course assignment
  Advice for report

## Slide 10: Toolchain
Vivado 2019.2
  General develop flow: Simulate HDL files, Synthesis, Implementation, Generate bitstream
DVT Eclipse
  get rid of Vivado useless integrated editor
VS Code
  a not bad choice to replace DVT but it takes some time to configure

## Slide 11: Toolchain
This page tells you some unnecessary auxiliary tools
MARS(MIPS Assembly Runtime Simulator)
  run the code in single step
  view all the registers’ value in GUI
QEMU(Quick EMUlator)
  run your own program in this fast, open source emulator
  use this tool through command line
MTI Bare Metal Toolchain --- compile the assembly code

## Slide 12: To-Do Lists
Intro
  Grammar(Verilog and SystemVerilog)
  Architecture
  Toolchain
Hand on
  Why our simulation don’t pass?
  Add instruction
  Run monitor program
Course assignment
  Advice for report

## Slide 13: Comparison Mechanism（比对机制）
Q:
  How to confirm that CPU runs correctly?
A:
  The aim of program is always to change the value of register(or memory).
  Compare our CPU executing results with the GS132(reference).
Core
=
Ref.
REG
FILE
PASS/FAIL

## Slide 14: Comparison Mechanism（比对机制）
If our CPU’s information is different from the reference, or when the CPU runs in a wrong loop, the simulation will stop

## Slide 15: Run Behavioral Simulation
Change the path of trace file in testbench

## Slide 16: Filed To Run The Program
Change the path of trace file in testbench
Now begin debugging happily :)

## Slide 17: Why Our Simulation Don’t Pass?
Step 1: Check the lab3.s
  a file translate .bin to assembly code with other information（反汇编）
  an important file to find the bug!
Step 2: Find the instruction according to PC
GET IT! ADDI

## Slide 18: Why Our Simulation Don’t Pass?
Step 3: Check the instruction set definition
  Find the operands in Vivado wave window
0151e5c0
0000b945
01529f05
+
=

## Slide 19: Why Our Simulation Don’t Pass?
Step 3: Check the instruction set definition
  Find the operands in Vivado wave window
0151e5c0
0000b945
01529f05
+
=
1011_1001_0100_0101(H) = -18107(D)

## Slide 20: Why Our Simulation Don’t Pass?
Step 4: Edit code
  Where the exe_i_src2 is assigned?

## Slide 21: Run Simulation Again
What is result? :)

## Slide 22: To-Do Lists
Intro
  Grammar(Verilog and SystemVerilog)
  Architecture
  Toolchain
Hand on
  Why our simulation don’t pass?
  Add instruction
  Run monitor program
Course assignment
  How to accomplish it

## Slide 23: Add Instruction
Consider SLT
  Read the definition of this inst.

## Slide 24: Add Instruction
Consider SLT
  Read the definition of this inst.

## Slide 25: Add Instruction
Step 1: Decide the type of the inst.
Step 2: Decide the regfile read address
Step 3: Decide the data format of source operand
  src1 is always $Rs, and needn’t change format
  src2 is from $Rt or immediate(original / 0 extend / signed extend)
Step 4: Decide alutype
Step 5: Decide aluop
…

## Slide 26: After Modification
We have corrected ADDI and implemented SLT, it’s fantastic!
  So what about accomplish a CPU in 1 month?
Run simulation again, see the result
  does the CPU pass the test?
Oooo god! There’s something wrong…

## Slide 27: Boss In Lecture 01 --- BGTZ

## Slide 28: To-Do Lists
Intro
  Grammar(Verilog and SystemVerilog)
  Architecture
  Toolchain
Hand on
  Why our simulation don’t pass?
  Add instruction
  Run monitor program
Course assignment
  How to accomplish it

## Slide 29: Run Monitor Program
Term
Serial
Kernel
Kernel Code
Kernel Data
User
Code
User
Data
BUS
监控程序的介绍及命令使用参考官方文档
监控程序的实现原理

## Slide 30: Run Monitor Program
To run the program, load all the memory in FPGA

## Slide 31: To-Do Lists
Intro
  Grammar(Verilog and SystemVerilog)
  Architecture
  Toolchain
Hand on
  Why our simulation don’t pass?
  Add instruction
  Run monitor program
Course assignment
  Advice for report

## Slide 32: Advice For Report
处理器研究的重要性
  芯片的研究意义
国内外研究现状
  通用处理器（RISC-V、香山、“一生一芯”、BOOM、玄铁…）
  图形处理器（GPU）
  AI 处理器（寒武纪、晟腾…）
调研资料
  龙芯杯 wiki，往届优秀作品
  书籍
    《自己动手写 CPU》《计算机系统设计：基于FPGA的RISC处理器设计与实践》
    《计算机体系结构：量化研究方法》《计算机组成与设计：硬件/软件接口》
    《超标量处理设计》…

## Slide 33: End & CU~
Lecture 01